## Slide 1
1
AquaClear
Underwater Image Restoration & Enhancement
CENG 455 – Digital Image Processing · Istanbul Arel University
Khaled Noaman · 200303812 · Spring 2026

## Slide 2
2
Contents
01
Introduction
Physics of underwater light degradation
02
Main Topic
The AquaClear Processing Pipeline
03
Results
Visual Before & After Comparisons
04
Conclusion
Key Takeaways and Future Work
05
References
Academic Sources

## Slide 3
3
01
Introduction
The physics of underwater light degradation

## Slide 4
4
Why Underwater Images Are Degraded
Color Attenuation
Red light (650nm) is completely absorbed within just 3–5m of depth. Only blue/green light survives, creating the pervasive cyan cast seen in all raw underwater photos.
Backscattering
Ambient light reflects off suspended particles (marine snow, plankton) directly into the camera lens, creating a dense gray-blue fog that eliminates visibility.
Forward Scattering
Light reflecting off the subject is scattered by particles before reaching the lens, blurring edges and destroying high-frequency details.

## Slide 5
5
The Jaffe-McGlamery Optical Model
The dominant model for underwater image formation states that the radiance captured by a camera sensor is the sum of three physical components:
E_total = E_direct + E_forward_scatter + E_backscatter
Direct Signal
Unscattered light from the object — the 'true' signal we want.
Forward Scatter
Deflected signal rays causing blur at the subject level.
Backscatter (Haze)
Ambient particles deflecting light directly into the lens as fog.

## Slide 6
6
Classical IP vs Deep Learning
Classical Image Processing ✓
Deep Learning / CNNs ✗
✓ Zero hallucinations — no invented pixels
✗ Frequently hallucinates textures
✓ Needs no training data
✗ Requires huge paired raw/clear datasets
✓ Fully transparent and mathematically auditable
✗ Black-box, unexplainable outputs
✓ < 0.5 sec on CPU, no GPU required
✗ Requires GPU, minutes per frame
✓ Safe for scientific measurement
✗ Risky for biological classification

## Slide 7
7
02
Main Topic
The AquaClear Processing Pipeline — Step by Step

## Slide 8
8
The AquaClear Pipeline
1
Auto-Analysis
Scans the image matrix to detect blur, haze, and color deficit levels, then sets optimal parameters.
2
Noise Reduction
Non-linear Bilateral Filter selectively smooths flat areas while protecting sharp edges.
3
Color Correction
Gray World Theorem scales the Red channel gain to neutralize the blue-green cast.
4
Dehazing
Dark Channel Prior estimates & subtracts backscattered transmission fog.
5
Contrast (CLAHE)
Adapative Histogram Equalization on the L channel of LAB color space.
6
Sharpening
Unsharp Masking boosts high-frequency edge data to restore detail lost to forward scattering.

## Slide 9
9
Phase 1: Auto-Analysis Heuristics
Static pipelines fail because every ocean differs. AquaClear dynamically calibrates for each image:
Red Deficit
b_mean - r_mean → if > 30: aggressive color correction
Haze Level
Dark Channel Mean / 255 → if > 0.4: omega = 0.98 (dense fog)
Blur Level
Laplacian Variance → if < 100: switch to NL-Means + heavy sharpening
Contrast
Grayscale Std Dev → if < 20: CLAHE Clip = 5.0 (very low contrast)

## Slide 10
10
Phase 3: Color Correction
Gray World Theorem: In a scene with diversity, average R = G = B = Gray
Algorithm:
r_mean, g_mean, b_mean = mean of each channel
total_mean = (r_mean + g_mean + b_mean) / 3
r_gain = total_mean / r_mean ← (boosts red)
R_corrected = clip(R * r_gain, 0, 255)
This single operation removes the dominant cyan tint by digitally restoring the wavelengths that water physically absorbed. Without it, the dehazing step cannot function correctly.

## Slide 11
11
Phase 4: Dark Channel Prior Dehazing
Step 1
Compute Dark Channel
D(x) = min of pixel across all 3 channels in a local patch
Step 2
Estimate Atmospheric A
Brightest 0.1% of pixels in the Dark Channel = Airlight (A)
Step 3
Calculate Transmission
t(x) = 1 – ω × min(I(y)/A) | ω controls strength
Step 4
Recover Scene Radiance
J(x) = (I(x) – A) / max(t(x), 0.1) + A

## Slide 12
12
Phase 5: CLAHE on LAB L-Channel
Why LAB color space?
LAB separates Luminance (L) from color (A, B channels). Equilizing R, G, B independently shifts color ratios and creates false hues. Equalizing only L preserves the restored colors from Phase 3.
Why CLAHE not Global HE?
Global HE stretches the entire image uniformly — in dark underwater scenes it creates massive noise artifacts in flat water regions. CLAHE divides the image into 8×8 tiles and limits the histogram peak (Clip Limit), boosting local contrast while preventing noise explosion.

## Slide 13
13
System Architecture
HTML/CSS/JS Frontend
Upload UI, Dark Mode, Before/After sliders, Metric gauges
→
Node.js Express Server
Multi-part upload, child-process forking, JSON routing
→
Python IP Engine
NumPy / OpenCV matrix processing. All 6 pipeline phases.

## Slide 14
14
03
Results
Visual Before & After Restoration Comparisons

## Slide 15
15
Results: Coral Reef
BEFORE – Raw Underwater Input
AFTER – AquaClear Enhanced

## Slide 16
16
Results: Jellyfish
BEFORE – Raw Underwater Input
AFTER – AquaClear Enhanced

## Slide 17
17
Results: Deep Ocean Wreck
BEFORE – Raw Underwater Input
AFTER – AquaClear Enhanced

## Slide 18
18
Results: Tropical Fish
BEFORE – Raw Underwater Input
AFTER – AquaClear Enhanced

## Slide 19
19
Results: Underwater Reef
BEFORE – Raw Underwater Input
AFTER – AquaClear Enhanced

## Slide 20
20
Objective Quality Evaluation Metrics
PSNR
Peak Signal-to-Noise Ratio
10·log₁₀(MAX² / MSE)
20–35 dB (Higher = Better Fidelity)
SSIM
Structural Similarity Index
Luminance × Contrast × Structure
0.80–0.95 (Higher = Less Distortion)
Entropy
Shannon Information Density
–Σ P(i)·log₂P(i)
+15–25% increase (More scene detail)
Colorfulness
C = √(σRG² + σYB²) + 0.3·√(μRG² + μYB²)
Per-channel saturation variance
Strong increase vs raw cyan image

## Slide 21
21
04
Conclusion
Achievements, Limitations, and Future Directions

## Slide 22
22
Conclusion
Successfully engineered a full 6-phase classical image processing pipeline tailored to aquatic optics.
Achieved real-time restoration (< 0.5 seconds) on standard CPU hardware — no GPU required.
Auto-analysis heuristic engine adaptively tunes all parameters per image, removing the need for manual tuning.
Objective metrics (PSNR, SSIM, Entropy) confirmed structural fidelity and genuine information recovery.
Wrapped the engine in a modern dark-themed web application with live Before/After visualization.
Limitations & Future Work
Gray World fails on monochromatic single-subject shots.
DCP struggles with artificial dive lights.
Future: Stereo depth mapping for per-pixel attenuation.
Future: CUDA port for live 60fps video telemetry.
Future: Mobile deployment for handheld dive cams.

## Slide 23
23
05
References
Academic & Technical Sources

## Slide 24
24
References
[1]
R. C. Gonzalez and R. E. Woods — Digital Image Processing, 4th ed.
Pearson, 2018
[2]
G. Bradski — The OpenCV Library
Dr. Dobb's Journal of Software Tools, 2000
[3]
K. He, J. Sun, and X. Tang — Single Image Haze Removal Using Dark Channel Prior
IEEE Transactions on PAMI, 2011
[4]
J. S. Jaffe — Computer Modeling and Design of Optimal Underwater Imaging Systems
IEEE Journal of Oceanic Engineering, 1990
[5]
A. M. Reza — Realization of CLAHE for Real-Time Image Enhancement
Journal of VLSI Signal Processing, 2004

## Slide 25
25
Thank You
Questions & Discussion
Khaled Noaman • 200303812
CENG 455 • Istanbul Arel University • Spring 2026